## Slide 1: Analog and Digital Signals

## Slide 2: Todays Topics
What’s the difference between analog and digital signals
Review Electricity Equations
General Purpose Input / Output (GPIO)
Pulse Width Modulation (PWM)
Analog to Digital Converters (ADC)
Microcontrollers and Computer

## Slide 3: Electronic Signals
Image from http://autosystempro.com/analog-and-digital-principles/

## Slide 4: Analog and Digital
Digital devices can only store digital signals
  Using 1 or several bits / sample
We store an array of numbers
Parameters
  Bits per sample
  Sampling rate
Example: Audio…
Image from http://www.centerpointaudio.com/Analog-VS-Digital.aspx
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 5: Bits per sample
Using just 1 bit
  Just 2 possible values/states: LOW (0) and HIGH (1)
  digital
Using >1 bit ( n bits where n>1)
  2n possible values/states
Example: using 3 bits:
  23 = 8 possible values/states
Called Quantisation
More bits -> higher resolution -> higher accuracy

## Slide 6: Sampling
Sensor signals are analog
  Temp -> voltage -> value
Sampling Rate
  Higher sampling rate( frequency) will give higher the accuracy
Image from http://www.snotmonkey.com/work/school/405/overview.html
Image from http://www.jazzpoparkisto.net/audio/audio32.html

## Slide 8: Analog and Digital Convertsion
Measure voltage
Parameters
  Bits per sample
  Sampling rate
For 1 bit we have …
  GPIO Input
For n bits we have …
  0 – 2n-1
Image from http://www.centerpointaudio.com/Analog-VS-Digital.aspx

## Slide 9: Electricity Equations

## Slide 10: Ohm’s Law

## Slide 11: Kirchhoff Law I

## Slide 12: Kirchhoff’s Law II

## Slide 13: Voltage Divider
This Photo by Unknown Author is licensed under CC BY-SA
If current in output wire is 0, then:

## Slide 14: Voltage Divider

## Slide 15: Voltage Divider

## Slide 16: Voltage Divider

## Slide 17: Voltage Divider

## Slide 18: Voltage Divider
SHORT CIRCUIT!

## Slide 19: Development Boards

## Slide 20: Microcontrollers (e.g. Arduino)
Simple, low cost
Runs one software program
Connect sensors/hardware via GPIO
Constrained Resources
  Low speed
  small memory
  (usually) no disk
  No general audio/video/networking (added as needed)
PWM
Can have built in Analog to Digital Conversion.
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 21: Single Board Computers (e.g. Rpi)
CPU
Memory and Storage
General interfaces for audio/video
Operating System
General Purpose Input and Output
Usually no built in ADC.
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 22: Output and Input on RPi
Digital Pins
  Value LOW (0) or HIGH (1)
Write programs to set pins to Low(0) or High(1)
  0V or 3.3V
Write programs to read pin values
  High(1)
  Low(0)

## Slide 23: Output
3.3V(HIGH) or 0V(LOW)
  Default 8 mA max per pin.
Switching a pin High is like connecting a 3.3V battery to device.
Switching a pin Low is like disconnecting the battery
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 24: Input
Can be Voltage Divider Circuit
Can measure Vout…
  via analogue input on Arduino
  Required Analog to Digital converter on RPi. (unless you want it to act like a switch)
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 25: Pulse With Modulation

## Slide 26: Pulse Width
We set the % of “high” cycle
  0 – 0%
  255 – 100%
    Typical for Arduino. Depends on the library
Implementation
  Hardware
  Software
Usage
  LED dimming
  Servo Motors
Arduino's PWM frequency at about 500Hz, the green lines would measure 2 milliseconds each.
Notes: Pulse Width Modulation, or PWM, is a technique for getting analog results with digital means. Digital control is used to create a square wave, a signal switched between on and off.
In the graphic below, the green lines represent a regular time period. This duration or period is the inverse of the PWM frequency. In other words, with Arduino's PWM frequency at about 500Hz, the green lines would measure 2 milliseconds each. A call to analogWrite() is on a scale of 0 - 255, such that
analogWrite(255) requests a 100% duty cycle (always on), and analogWrite(127) is a 50% duty cycle (on half the time) for example.

## Slide 27: Microcontrollers and Computers

## Slide 28: Microcontrollers and computers
Firmware
Software